Computer Architecture
Ch2 – Computer System Organization
Nguyễn Quốc Đính, FIT – IUH
HCMC, Aug 2015

---
Computer System Organization
- Processor
- Memory (bit, byte, address, ECC, cache, RAM, ROM, RAID, CD ...)
- I/O (terminal, printer, modems, ASCII)
- Buses
The organization of a simple computer with
one CPU and two I/O devices

---
Central Processing Unit (CPU)
CPU function is to execute programs stored in the main memory
- fetching instructions
- examining instructions
- executing them one after another
The organization of a simple computer with
one CPU and two I/O devices

---
CPU Organization
- Data path consists of:
  - Registers (No 1 – 32)
  - Arithmetic Logic Unit
  - Buses
- Data path cycle is the hart of most CPU
The data path of a typical Von Neumann machine.

---
Instruction Execution Steps
1. Fetch next instruction from memory into instruction register
2. Change program counter to point to next instruction
3. Determine type of instruction just fetched
4. If instructions uses word in memory, determine where it is
5. Fetch the word, if needed, into CPU register
6. Execute the instruction
7. Go to step 1 to begin executing following instruction
Fetch – decode – execute cycle

---
Interpreter (1)
…
An interpreter for a simple computer (written in Java).

---
Interpreter (2)
…
An interpreter for a simple computer (written in Java).

---
CISC
(Complex Instruction Set Computer)
- Origin:
  - Initial instruction set and computer architecture
  - Hardware designed to facilitate software languages and programming
- Instruction
  - Complex, defined based on software and/or application requests
- CPI (cycles per instruction)
  - Increase with instruction complexity

---
CISC
(Complex Instruction Set Computer) – cont'd
- Classic CISC processor
  - Motorola 68000
  - Intel 8088, 8086, 80286
- Early CISC got out of hand
  - How to get more accomplished faster? One way is to reduce CPI
  - < 10% of instruction execute 90% of the time … results in wasted hardware and large size

---
The architecture fix to early CISC
- To reduce the CPI, the instructions had to get easier and faster
  - CPI = 1 goal
  - Instructions should be easily decoded (fewer, simpler instruction)
- Memory accesses are slow and a major processor speed impediment
  - Add more register for fewer memory access
  - Force to use register by limiting memory access to load and store
Result in a “Reduced Instruction Set Computer” (RISC)

---
RISC
Reduced Instruction Set Computer
- Origin:
  - 1980 Berkeley: David Patterson and Carlo Sequin
  - 1981 Stanford: John Hennessy
- Addressing
  - Load/Store
- Instruction:
  - Fixed length (typically word length), minimal format

---
Design Principle for Modern Computers
(RISC design principle)
- All instructions directly executed by hardware
  - Eliminate a level of interpretation provides high speed for most instructions
- Maximize rate at which instructions are issued
  - Increase number of instructions per second (MIPS)
  - Parallelism can play a major role in improving performance

---
Design Principle for Modern Computers
(RISC design principle) – cont'd
- Instructions should be easy to decode
  - Making instruction regular, fixed length.
  - Fewer different formats for instruction, the better
- Only loads, stores should reference memory
  - Most instruction come from/return to CPU registers
  - Only LOAD, STORE instructions should reference memory
- Provide plenty of registers
  - At least 32 registers

---
If RISC was so great,
why did CISC still exist?
- Backward compatibility
- CISC instructions set with RISC micro-operation execution cores

---
Speed up CPU computing capacity?
- Increasing clock speed.
  - Up-bound?
- Parallelism
  - Instruction-level parallelism (ILP)
  - Processor-level parallelism (PLP)

---
Speed up CPU computing capacity?
- Increasing clock speed. Up-bound?
- Parallelism
  - Instruction-level parallelism (ILP)
  - Processor-level parallelism (PLP)

---
Instruction-Level Parallelism
1. A five-stage pipeline
2. The state of each stage as a function of time. Nine clock cycles are illustrated

---
Dual Pipeline
- If one pipeline is good, then surely two pipelines are better
- Pentium processor has two five-stage pipelines
Dual five-stage pipelines with a common instruction fetch unit

---
Dual Pipeline
- Pentium two-issue superscalar
  - U-pipeline (main): execute all Pentium instructions
  - V-pipeline (sub): execute simple Pentium instr. when there are no conflicts
Dual five-stage pipelines with a common instruction fetch unit

---
Multi-Pipeline?
- More than 2 pipeline is so complicated
- Different approach:
  - Instruction issue rate is much higher than the execution rate, then the workload spread across a collection of functional units
  - CPU with 100ns clock ↔ CPU with 400ns clock that issues 4 instructions per cycle.

---
Superscalar Processor
Stage 4 have functional units take longer than one clock cycle to execute (e.g access memory, floating-point arithmetic)
A superscalar processor with five functional units
Pentium II concept

---
Speed up CPU computing capacity?
- Increasing clock speed. Up-bound?
- Parallelism
  - Instruction-level parallelism (ILP)
  - Processor-level parallelism (PLP)

---
Processor-level Parallelism (1)
An array of processor of the ILLIAC IV type
(first array processor at UIUC 1972)

---
Processor-level Parallelism (2)
A single-bus multiprocessor.
A multicomputer with local memories.

---
Primary Memory
Memory Addresses
Given 2^10 bits, how is the memory organized:
1024 1-bit cells
128 8-bit bytes
64 16-bit words
32 32-bit words
Each could have a different means of addressing: bit-level, byte-level, word(?)-level ...

---
Primary Memory
Memory Addresses
Three ways of organizing a 96-bit memory

---
Primary Memory
Memory Addresses
A memory with 2^12 cells of 8 bits each and a memory with 2^12 cells of 64 bits each need 12-bit addresses
Number of bits per cell for some historically
interesting commercial computers

---
Primary Memory
Memory Addresses
- Note:
  - Most PC based processors use byte-addressing
  - Others use word-addressing, particularly DSP and microcontroller
A byte-addressable 32-bit (memory addresses) computer can address 2^32 = 4GB
Intel 8086 (16-bit) supported 20-bit addressing, allowing it to access 1 MiB.

---
Primary Memory
Memory Addresses
- When a modern computer reads from or writes to a memory address, it will do this in word sized chunks
- Byte aligned storage is typically required
  - 16-bit words start at multiple of 2
  - 32-bit words start at multiple of 4
  - If not?

---
Alignment
struct mydata {
int a;	//4
char b;	//1
int c;	//4
char d;	//1
char e;	//1
float t;	//4
};
?
cout<<"Size = " << sizeof(mydata) <<endl;
struct mydata2 {
  double x;	//4
  char n[1];	//
};
?
cout<<"Size = " << sizeof(mydata2) <<endl;

---
Padding
padding = (align - (offset mod align)) mod align
new offset = offset + padding
Typical padding
A char (one byte) will be 1-byte aligned.
A short (two bytes) will be 2-byte aligned.
An int (four bytes) will be 4-byte aligned.
A long (four bytes) will be 4-byte aligned.
A float (four bytes) will be 4-byte aligned.
A double (eight bytes) will be 8-byte aligned on Windows and 4-byte aligned on Linux (8-byte with -malign-double compile time option).
Any pointer (four bytes) will be 4-byte aligned. (e.g.: char*, int*)
See http://en.wikipedia.org/wiki/Data_structure_alignment

---
Byte Ordering
Big endian vs Little endian
From http://en.wikipedia.org/wiki/Endianness

---
Byte Ordering
Big endian vs Little endian
(a) Big endian memory (b) Little endian memory

---
Byte Ordering
Big endian vs Little endian
Question: illustrate following struct memory organization under big-endian and little-endian machine
struct {
char c	//(“A”)
int i	//(21)
}

---
Byte Ordering
Big endian vs Little endian
Question: illustrate following struct memory organization under big-endian and little-endian machine
(char*) JIM SMITH
(int) 21
(int) 260

---
Byte Ordering
Big endian vs Little endian
Name:(Char*) JIM SMITH
Age:(int) 21
Department:(int) 260
(a) Big endian memory
(b) Little endian memory

---
Problem
Write a C/C++ program to determine the current running computer is big-endian or little-endian

---
Why is this really importance?
Big endian	Little endian
SPARC (Sun Micro) / Motorola 68000 / PowerPC	Intel / IBM(typically)
“Well-known processor architectures that use the little-endian format include:
x86 (including x86-64), 6502 (including 65802, 65C816), Z80 (including Z180, eZ80 etc.), MCS-48, 8051, DEC Alpha, Altera Nios, Atmel AVR, SuperH, VAX, and, largely, PDP-11.”
“Well-known processors that use the big-endian format include:
Motorola 6800 and 68k, Xilinx Microblaze, IBM POWER, and System/360 and its successors such as System/370, ESA/390, and z/Architecture.”
Bi-endian: ARM versions 3 and above, PowerPC, Alpha, SPARC V9, MIPS, PA-RISC and IA-64
From http://en.wikipedia.org/wiki/Endianness

---
Error Correcting Codes (1)
- The bits in a data transfer can become corrupted.
  - More likely with modem or wireless transmission
  - Bus can have bit errors!
- If you expect there to be a high probability that bits in a byte/word will be corrupted, encode!

---
Error Correcting Codes (2)
- Parity Bit
  - For EVEN parity, the sum of all the bits must be even (0110 = 0+1+1+0=2)
  - For ODD parity, the sum of all the bits must be odd (1011 = 1+0+1+1=3)
  - One more bit is added to the binary data to make the “bit field” EVEN or ODD
- Notes
  - It works really well with 7-bit ASCII to create an 8-bit word !
  - Also 9-bit memory ICs, used for 8-bits and parity

---
Memory Hierarchy Pyramid
Single clock cycle access
Multiple clock cycles access
10's – 100's clocks cycle access
100's clock cycles
access or more
Removable disks. 1000's clock
cycles access or more
“Overnight achieves”

---
Processor-DRAM Latency Gap

---
Cache Memory
- Fact:
  - CPU goes in vertical
  - Memory goes in horizon
- Build memory inside CPU chip?
  - Cost
- Combination?
  - Small amount of fast memory
  - Large amount of slow memory

---
Cache Memory
- Observation: 90% time to execute 10% instructions overall
- Idea: the most heavily used memory words are kept in the cache. When the CPU need a word, it first looks in the cache

---
Basic Cache Algorithm for Load

---
Average Memory Access Time
Registers and Main Memory (1)

---
Average Memory Access Time
Registers and Main Memory (2)
Average memory access time
Where:
Defined:

---
Average Memory Access Time
Registers and Main Memory (3)
t_{aa} = ?
Defined:

---
Average Memory Access Time
Registers, Cache, and Main Memory (1)

---
Average Memory Access Time
Registers, Cache, and Main Memory (2)
Average memory access time
Where:

---
Average Memory Access Time
Registers, Cache, and Main Memory (3)
Defined:
t_{aa} = ?

---
Average Memory Access Time
L1, L2 Cache, and Main Memory (1)

---
Average Memory Access Time
L1, L2 Cache, and Main Memory (2)

---
Cache Memory
- Modern machines typically have split L1 caches.
  - Level 1 Instruction Cache: Optimized for threads of execution, support for branching, integrated with intelligent instruction fetch and preprocessing units. Focus on filling from higher level caches and main memory. It does not typically need to write-back instruction to main memory.
  - Level 1 Data Cache: Optimized for data handling. Facilitate data fetching for computations and data write back of results.
- Therefore, the cache controllers are concerned about different “cache policies and procedures”.

---
Mapping Functions
- Cache of 64kByte
- Cache block of 4 bytes
  - i.e. cache is 16k (214) lines of 4 bytes
- 16MBytes main memory
  - 24 bit address
  - (22^4=16M)

---
Direct Mapping
- Each block of main memory maps to only one cache line
  - i.e. if a block is in cache, it must be in one specific place
- Address is in two parts
- Least Significant w bits identify unique word
- Most Significant s bits specify one memory block
- The MSBs are split into a cache line field r and a tag of s-r (most significant)

---
Direct Mapping: Address Structure
- 24 bit address
- 2 bit word identifier (4 byte block)
- 22 bit block identifier
  - 8 bit tag (=22-14)
  - 14 bit slot or line
- No two blocks in the same line have the same Tag field
- Check contents of cache by finding line and checking Tag
Tag s-r
Line or Slot r
Word w
8
14
2

---
Direct Mapping: From Cache to Memory

---
Direct Mapping: Cache Line Table
Cache line	Main Memory blocks held
0	0, m, 2m, 3m…2s-m
1	1,m+1, 2m+1…2s-m+1
…
m-1	m-1, 2m-1,3m-1…2s-1

---
Direct Mapping: Cache Organization

---
Direct Mapping: Summary
- Address length = (s + w) bits
- Number of addressable units = 2^(s+w) words or bytes
- Block size = line size = 2^w words or bytes
- Number of blocks in main memory = 2^(s+ w)/2^w = 2^s
- Number of lines in cache = m = 2^r
- Size of tag = (s – r) bits

---
Direct Mapping: Pros & Cons
- Simple
- Inexpensive
- Fixed location for given block
  - If a program accesses 2 blocks that map to the same line repeatedly, cache misses are very high

---
Victim Cache
- Lower miss penalty
- Remember what was discarded
  - Already fetched
  - Use again with little penalty
- Fully associative
- 4 to 16 cache lines
- Between direct mapped L1 cache and next memory level

---
Associative Mapping (AM)
- A main memory block can load into any line of cache
- Memory address is interpreted as tag and word
- Tag uniquely identifies block of memory
- Every line’s tag is examined for a match
- Cache searching gets expensive

---
AM: Cache to Memory

---
Fully Associative Cache Organization

---
AM: Address Structure
- 22 bit tag stored with each 32 bit block of data
- Compare tag field with tag entry in cache to check for hit
- Least significant 2 bits of address identify which 16 bit word is required from 32 bit data block
- e.g.
  - Address	Tag	Data	Cache line
  - FFFFFC	FFFFFC	24682468	3FFF
Tag 22 bit
Word
2 bit

---
AM: Summary
- Address length = (s + w) bits
- Number of addressable units = 2^(s+w) words or bytes
- Block size = line size = 2^w words or bytes
- Number of blocks in main memory = 2^(s+ w)/2^w = 2^s
- Number of lines in cache = undetermined
- Size of tag = s bits

---
Memory Hierarchy Pyramid (again)
Single clock cycle access
Multiple clock cycles access
10's – 100's clocks cycle access
100's clock cycles
access or more
Removable disks. 1000's clock
cycles access or more
“Overnight archieves”

---
IC Memory Types
- ROM
  - Read-only Memory
  - Permanent storage (boot code, embedded code)
- SRAM
  - Static Random Access Memory: cache and high speed access
- DRAM
  - Dynamic Random Access Memory: Main Memory
- EPROM
  - Electrically programmable read-only memory
  - Replace ROM when reprogramming required

---
IC Memory Types
- EEPROM
  - Electrically erasable, programmable read-only memory.
  - Alternative to EPROM, limited but regular reprogramming,
  - Device configuration info during power down
- FLASH
  - An advancement on EEPROM technology allowing blocks of memory location to be written and cleared at one time instead. Found in thumb drives/memory stick or as solid-state hard disks.
Note: EEPROM and FLASH have lifetime write cycle limitations!

---
Secondary Memory
Magnetic, CD …

---
Magnetic Disks
Electronic Coil Writing/Reading Magnetic Medium
Synchronization information
A portion of a disk track. Two sectors are illustrated.

---
Magnetic Disks
- Track
  - A radial spaced circle on a platter for storing data.
  - Typically 5,000 to 10,000 tracks per centimeter on a platter or 1-2 micron track widths.
- Sector
  - A fixed bit-length section of a track.
  - There are multiple sectors in a track.
  - A typical sector contains: a preamble, 512 Bytes or 4096 bits, and error correction code bits.
  - Between sectors on a track are inter-sector gaps.

---
Magnetic Disks
A disk with four platter

---
Magnetic Disks
A disk with five zones. Each zone has many tracks

---
Speed up the Transfers
Disk Controllers:
- Typically includes buffer memory space for rapid burst transfers.
- May (must) allow simultaneous access to the multiple tracks in a cylinder.
- Performs the ECC generation, testing, and corrections
- Can provide a mapping table of good and bad sectors.

---
ATA vs SATA vs SCSI
- IDE → EIDE → ATA → SATA: IDE disks
- SCSI disk
  - Differ from IDE disk in the interface
  - Higher data rate
  - More than one devices in the bus can operate (compare to 1 active device of IDE/EIDE)
- Current trend: SATA

---
RAID (1)
Redundant Array of Inexpensive Disks
Example from Intel Modular, a strong web server
CPU: 2 x Intel® Nehalem-EP Xeon Quad Core Gainestown E5520 ( 2.26GHz 8-Threads 2x6.4GT/s 8MB(L3))
RAM: Kingston DDR3 PC-8400 12GB/1066/Ecc/Reg Intel Certifield
HDD: 14 x Seagate 2.5" 300G/SAS/10Krpm Version 2.0 (RAID 5)

---
Note: Hard disk provides low bandwidth and is quite easily to fail!
Ideas: Use a box full of hard disks to allow:
Higher data transfer and storage rates (operate disks in parallel)
Higher degrees of redundancy (save on multiple disks simultaneously), and
Higher degree of error detection and correction (Additional ECC)

---
RAID (2)
Redundant Array of Inexpensive Disks
    RAID levels 0 through 2.
Backup and parity disks are shown shaded.

---
RAID (3)
Redundant Array of Inexpensive Disks
Level	Description	Feature
RAID 0	Block-level striping	Speed Increase
RAID 1	Mirroring	Redundancy
RAID 2	Bit-level striping with error-correcting code / Drives were synchronized	Faster with conditional 1 drive failure recovery

---
RAID (4)
Redundant Array of Inexpensive Disks
RAID levels 3 through 5.
Backup and parity disks are shown shaded.

---
RAID (5)
Redundant Array of Inexpensive Disks
Level	Description	Feature
RAID 3	Byte-level striping with parity / (Simple version of level 2)	Faster with 1 drive failure recovery (with parity bit?)
RAID 4	Block-level striping with parity (XOR calculation)	Faster with 1 drive failure recovery
RAID 5	Block-level striping with distributed parity / Eliminated the bottleneck of parity disk in level 4	Faster with conditional 1 drive failure recovery

---
Question
- How ECC with parity bit in RAID level 3 has “recovery” feature?
- Why RAID level 4 and RAID level 5 utilize XOR function but not AND or OR?
- Why RAID level 5 is considered to be more fairly distributing in utilizing among disks than level 4?
- Total storing capacity of n disk in RAID level 0, 1, 2, 3, 4, and 5?

---
CD-ROM
Recording structure
of CD-ROM
Bit=1 Transitions from pit to land OR transitions from land to pit
Bit=0 No transition of the data.

---
CD-ROM
Logical data layout on a CD-ROM

---
CD Storage Requirement
- Audio Format Storage Requirement:
74 min. Audio: 44,100 samples/channel/second x 2 bytes/sample x 2 channels x 74 minutes x 60 seconds/minute = 783,216,000 bytes
80 min. Audio: 44,100 samples/channel/second x 2 bytes/sample x 2 channels x 80 minutes x 60 seconds/minute = 846,720,000 bytes

---
Operating Rate
http://en.wikipedia.org/wiki/CD_and_DVD_writing_speed

---
DVD
- Name
  - Digital Video Disk (originally)
  - Digital Versatile Disk (now)
- A higher density version of the CD.
  - Smaller pits
  - Tighter spiral
  - Different laser with a reduced spot size (more expensive)
  - Advanced versions with multiple layers (dual layer, top and bottom)

---
Operating Rate
- Total Data: 4.7 GB (single-sided, single layer)
  - 133 min of 720x480 high-resolution video, 8-language sound track, and 32 subtitles. (Fit 92% of all Hollywood movies)
- Potential DVD Capacities:
  - Single-sided, single layer	4.7 GB
  - Single-sided, dual layer	8.5 GB
  - Double-sided, single layer	9.4 GB
  - Double-sided, dual layer	17.0 GB

---
Blue-Ray
http://www.howstuffworks.com/blu-ray.htm

---
Input/Output
Bus, Terminal, Mice, Printer, Tel Com

---
Single Bus System
Old Omnibus, Unibus, Single-bus System

---
Aspects of Bus
- One operation at a time
  - Buses include address/data/control
  - Bus multiplex on one cycle with data on the next
- DMA
  - A controller that reads/write data to/from memory without CPU intervention is said to be performing Direct Memory Access (DMA)
- Bus arbiter
  - What if CPU, I/O controller want to use the bus at the same time?

---
Problems from Single Bus System
- The simple bus works well when all components ware roughly in balance
- Unbalance performance nowadays between components
- People tend to keep printer, scanner, modem when upgrading their PC
→ Solution: multiple buses

---
Multiple Bus System
A typical modern PC with a PCI bus and an ISA bus

---
Other version
Picture from http://computer.howstuffworks.com/pci1.htm

---
Bit-map terminals
Writing pixels to the screen (4:3 aspect ratios)
VGA	640 x 480 (480i)
SVGA	800 x 600
XVGA	1024 x 768
 1280 x 960
HD	1440 x 1080
 1600 x 1200
Writing pixels to a high definition screen (16:9 aspect ratios)
 640 x 360
 800 x 450
 1024 x 576
HD	1280 x 720 (720p)
 1600 x 900
HD	1920 x 1080 (1080i, 1080p)

---
Byte per Pixel
- 1
  - 2^8 levels or 256 colors (the levels for RGB)
- color palette
  - interpretation of 256 into whatever is fixed for the value ”indexed” color
  - reduce video RAM by 2/3
- 3
  - one byte for each color - 2^8 levels or 256 each 24-bit RGB representation

---
CRT Monitor
(CRT = Cathode Ray Tube)
(a) Cross section of a CRT
(b) CRT scanning pattern

---
Flat Panel Displays
(a) The construction of an LCD screen.
(b) The grooves on the rear and front plates are perpendicular to one another.

---
Printer
- Matrix printer
- Inkjet printer
- Laser printer

---
Telecommunication
- Modem
- DSL
- Ethernet

---
MODEM – Modulator/Demodulator
- Convert digital data 0’s and 1’s to audio tones.
- Allow data transmission on an analog phone line (audio) which allows tones from 50Hz to 3500 Hz
- Full-duplex vs Half-duplex
  - Full-duplex employs different frequencies

---
MODEM
Transmission of the binary number 01001010000100 over a
telephone line bit by bit. (a) Two-level signal. (b) Amplitude
modulation. (c) Frequency modulation. (d) Phase modulation.

---
Digital Subscriber Lines
- Low speed in dial-up connection due to filler in telco office (limit to 3000Hz)
- xDSL
  - Remove the filter
  - ADSL (Asymmetric DSL)
Asymmetric

---
Digital Subscriber Lines
A typical ADSL equipment configuration.

---
Internet over Cable
Frequency allocation in a typical cable TV system
used for Internet access
Properties:
- Hundreds of user share the same cable to the headend
- Asymmetric connection also

---
Digital Cameras

---
Digital Cameras
- Four CCD make up on pixel
  - 4 is more convenience than 3
  - Eye is more sensitive to green light than to red or blue light
  - Camera maker claim 6 mpixel, means 1.5 mpixel in real

---
Bonus
Hard Disk Access Time Calculation

---
Access Time (1)
- Seek time:
  - First the head must be position on the right track (radial distance).
  - Typical numbers: 5-15 msec.
  - “Avg. seek time”: not best case, not worst case, average!
  - Min. time – one track to the next
  - Max. time – outer track to inner track or vice versa

---
Access Time (2)
- Rotational Latency:
  - The head must arrive at the correct sector on a track (rotational distance)

---
Access Time (3)
- Access time = Seek time + Rotational time
- Example:
  - A drive with 8.9 msec avg. seek time at 7200 RPM (Western Digital WD800JBRTL drive)
  - Access Time = 8.9 msec + 4.17 msec = 13.07 msec.

---
Transfer Time
Example: If there are 16 or 64 sectors on a track and the rotation rate is 7200 RPM, what is the maximum possible data transfer rate to read one sector on the disk.
7200 RPM → 8.33 msec/rev
For 16 sectors → 8.33/16 = 0.52 msec/sector
4096 bits/sector → 4096/0.00052 = 7,876,923 bits/sec ~ 0.98 MB/sec.
7200 RPM → 8.33 msec/rev
For 64 sectors → 8.33/64 = 0.13 msec/sector
4096 bits/sector → 4096/0.00013 = 31,507,692 bits/sec ~ 3.94 MB/sec.
Note: this is the maximum burst rate
doesn't include access time to get data

---
Transfer Time
How does cylinder help?
Example: If there are 16 or 64 sectors on a track and the rotation rate is 7200 RPM, what is the maximum possible data transfer rate to read one sector on the disk.
0.98 MB/sec & 3.94 MB/sec.
- Note:
  - To support (or even get close to) ATA rates of 100-150 MB/sec and quoted WD rate, multiple tracks in a cylinder must be read simultaneously!
  - Multiply the rates defined by the number of surfaces simultaneously read, and higher rates can be achieved!

---
Example: Time to read one sector given as 10,800 RPM, 8.0 msec avg. seek time and 64 sectors per track.
Avg. Access Time = 8.0 msec + (5.56/2 msec) = 10.78 msec
Transfer time = 5.56 msec/rev / 64 sectors/rev = 0.0869 msec
Total Time = 10.78 msec + 0.0869 msec = 10.8669 msec
If this is the average data transfer rate we have,
4096 bits/10.8669 msec = 376,924 bits/sec or 46.01 kB/sec ... not very fast for “random sectors”
Fortunately, we usually read multiple sectors at a time (64).
Avg. Access Time = 8.0 msec + (2.78 msec) = 10.78 msec
Transfer time = 5.56 msec/rev / all sectors/rev = 5.56 msec
Total Time = 10.78 msec + 5.56 msec = 16.34 msec
64 x 4096 bits/16.34 msec = 16,043,084 bits/sec or 2.005 MB/sec ... much better

---
Copyright note
Slides are adopted form lecture notes of Tanenbaum, Structured Computer Organization, Fifth Edition, (c) 2006 Pearson Education, Inc.